## Slide 1: Silica Hazard Awareness
Notes: For Developing Countries

## Slide 2: Objectives
Define occupational safety and health
Provide background on what silica is and where it is present
Discuss where and how exposure to silica occurs
Describe the health effects related to silica
Discuss how you measure it
Describe how you control it

## Slide 3: Occupational Safety and Health
Occupational Safety and Health ( OSH)
  Occupational (Industrial) Hygiene-the anticipation, recognition, evaluation, control and prevention of hazards from work that may result in injury or illness
  Occupational Medicine-branch of medicine concerned with the maintenance of health in the workplace
    Includes prevention and treatment of work-related injuries and illnesses
    Secondary focus on maintaining and increasing productivity
Occupational (Industrial) Hygiene
Occupational Medicine
Occupational Health
Notes: https://en.wikipedia.org/wiki/Occupational_medicine
https://en.wikipedia.org/wiki/Occupational_hygiene

## Slide 4: Why is OSH Important?
Globally, 6,300 people die as a result of occupational injury or work-related disease every day
  More than 2.3 million deaths per year
  Tremendous impact on the global community- individuals, families, and employers
  Many injuries and diseases are preventable
Notes: According to the International Labour Organization, g

## Slide 5: Work related respiratory diseases
Occupational airborne particles and inhaled cancer-causing agents (i.e. carcinogens) are an important cause of death and disability worldwide
Silicosis, lung damage caused by scarring from silica dust, is the world’s oldest known occupational disease (around 400 B.C.)

## Slide 6
Notes: Picture here

## Slide 7: What exactly is silica?
Word | Definition
Silicon (Si) | Second most abundant element
Silica (Si + O2 ) | Combination of silicon and oxygen
Silicates (Si + O2 + metal) | Combination of silicon, oxygen and one or more metals
Silicone | Synthetic polymer with properties like rubber
Notes: Silica is a group of minerals, in which silicon and oxygen combine. Silicon and oxygen are the two most abundant elements in the earth’s crust. Silica is naturally occurring, and is generally separated into two types of silica.

## Slide 8: Forms of silica
Notes: The first, is a crystalline solid, whose components are uniformly arranged, as shown here. The other primary type of silica, is the amorphous solid form, where the molecules are randomly arranged.
https://sciencestruck.com/crystalline-vs-amorphous-solids-difference

## Slide 9: Types of silica dust in air
Silica
Si + O
crystalline
silica
amorphous
Silica
Notes: Crystalline silica causes long term disease, silicosis. There are three subsets of crystalline silica. Cristobalite, trydimite, and quartz. Christobalite and trydimite are rare forms of silica; however, quartz is very common, and has been more clearly shown to cause occupational disease. Therefore for the remainder of this talk, we will focus on quartz.

## Slide 10: Types of silica dust in air
Silica
Si + O
crystalline
silica
amorphous
Silica
Does not cause silicosis

## Slide 11: Types of silica dust in air
Silica
Si + O
crystalline
silica
amorphous
Silica
quartz
(common)
cristobalite
(less common)
tridymite
(less common)
Does not cause silicosis

## Slide 12: Types of silica dust in air
Silica
Si + O
crystalline
silica
amorphous
Silica
quartz
(common)
cristobalite
(less common)
tridymite
(less common)
large particles
small (respirable) particles
<10um
Does not cause silicosis

## Slide 13: Types of silica dust in air
Silica
Si + O
crystalline
silica
amorphous
Silica
quartz
(common)
cristobalite
(less common)
tridymite
(less common)
large particles
small (respirable) particles
<10um
Does not cause silicosis
no problem
PROBLEM!!!
Notes: Only crystalline silica causes disease. There are three subsets of crystalline silica. Cristobalite, trydimite, and quartz. Cristobalite and trydimite are rare forms of silica; however, quartz is very common, and has been more clearly shown to cause occupational disease.
Reed- I think I need your subject matter expertize here. 1. Why is amorphous not a problem. 2. Even if cristobalite
And trydimite are rare are they still not a problem?

## Slide 14: Silica
Crystalline silica is one of the most common minerals found in the earth's crust
  Naturally-occurring
Notes: https://phil.cdc.gov/phil/details.asp

## Slide 15: Silica
Crystalline silica is one of the most common minerals found in the earth's crust
  Naturally-occurring
  Incorporated into manmade materials
Notes: https://phil.cdc.gov/phil/details.asp

## Slide 16: Silica
Crystalline silica is one of the most common minerals found in the earth's crust
  Naturally-occurring
  Incorporated into manmade materials
  Used to manufacture products
Notes: https://phil.cdc.gov/phil/details.asp

## Slide 17: Silica
Crystalline silica is one of the most common minerals found in the earth's crust
  Naturally-occurring
  Incorporated into manmade materials
  Used to manufacture products
Silica is EVERYWHERE!
Notes: https://phil.cdc.gov/phil/details.asp

## Slide 18: International Concern over Silica
At least 227 million workers are employed in high risk industries worldwide
  Over 1 million children in these industries
Exposed people are often the most vulnerable, disadvantaged and medically underserved
Respirable crystalline silica (RCS) particles have been classified as an occupational airborne particulate of worldwide concern

## Slide 19: How do people get exposed?

## Slide 20: Industries where Exposures Occur
Mining & Quarry work

## Slide 21: Industries where Exposures Occur
Mining & Quarry work
Construction

## Slide 22: Industries where Exposures Occur
Mining & Quarry work
Construction
Manufacturing

## Slide 23: Industries where Exposures Occur
Mining & Quarry work
Construction
Manufacturing
Ceramics

## Slide 24: Industries where Exposures Occur
Mining & Quarry work
Construction
Manufacturing
Ceramics
Brick making

## Slide 25: Industries where Exposures Occur
Mining & Quarry work
Construction
Manufacturing
Ceramics
Brick making
Shipyards
Others

## Slide 26: Some Tasks with Airborne Exposure
Industries | Job Tasks
Manufacturing | Abrasive blasting, glass making, making soaps & detergents
Ceramics | Manufacturing clay, pottery
Construction | Sandblasting, rock drilling, masonry work, jack hammering, tunneling
Foundry work | Grinding, molding, shaking, core room
Mining | Cutting stone, drilling through rock
Railroad | Setting/laying track
Stone cutting | Sawing, abrasive blasting, chipping, grinding

## Slide 27: Exposure routes for silica
Primarily people are exposed by inhalation
  Skin exposure or ingestion (i.e. eating, drinking) are not of concern
Breathed in through the nose and mouth and can stay in the lungs for years
Smallest particles enter deep into the lungs

## Slide 28: Visible-vs-Respirable Dust
Visible dust contains large and small particles
  Tiny, respirable-sized particles (those that can get deep into the lungs) containing silica pose the greatest hazard and are not visible.
  Largest dust is trapped in the upper airways
If you see visible dust, respirable dust is also likely present!!!

## Slide 29
Think about your work environment.
Do silica exposures occur ?

## Slide 30: What happens to people if they get exposed?

## Slide 31: The big, small problem: small particles
Inhaling very small ("respirable") silica particles, causes multiple diseases, including silicosis
Silica also causes lung cancer and chronic obstructive pulmonary disease (COPD)
Exposure is also associated with kidney disease, autoimmune disease and contracting tuberculosis (TB)

## Slide 32: Diseases associated with Silica
Silica
TB
and other
mycobacterial infections
COPD
bronchitis
emphysema
Renal disease
silicosis
cancer
auto immune diseases
Notes: Bolded are those with clear epidemiologic evidence, renal disease and autoimmune disease have less strong associations.

## Slide 33: Diseases associated with Silica
Silica
TB
and other
mycobacterial infections
COPD
bronchitis
emphysema
Renal disease
silicosis
cancer
auto immune diseases
Disease may occur YEARS to DECADES later!!!
Notes: Bolded are those with clear epidemiologic evidence, renal disease and autoimmune disease have less strong associations.

## Slide 34: Diseases of Silica: Silicosis
Silica particles cause scarring and hardness of the lungs
  Scarring makes it hard for lungs to expand, making it difficult to breathe
Patients have cough, shortness of breath (SOB), weakness and tiredness
  May lead to death
Diagnosed by a work history and chest X-ray (CXR) +/- pulmonary function testing (PFTs)
  Often misdiagnosed as TB
Normal CXR
Small
parenchymal
opacities
Large
parenchymal
opacities
Notes: Bolded are those with clear epidemiologic evidence, renal disease and autoimmune disease have less strong associations.
https://www.cdc.gov/niosh/topics/chestradiography/ilo.html

## Slide 35: Diseases of Silica: Silicotuberculosis
TB is a highly contagious disease
  Silicosis increases the risk of TB by four times
Patients have cough (sometimes with blood), chest pain, SOB, and tiredness
  Deadly if untreated
Diagnosed by CXR or Sputum
Silicosis
Tuberculosis
Silicotuberculosis

## Slide 36: Diseases of Silica: Lung Cancer
International Agency for Research on Cancer (IARC) classifies silica as a known human carcinogen
Patients have cough, SOB, chest pain, coughing blood, tiredness, weight loss, etc.
  May lead to death
Diagnosed by symptoms and imaging
  CXR or Chest CT
Notes: https://visualsonline.cancer.gov/details.cfm?imageid=9029

## Slide 37: Diseases of Silica: COPD
Air is obstructed from getting out of the lungs, leaving less room to bring in oxygen
Patients may have a chronic cough, phlegm production, SOB and wheezing
  Often leads to exacerbations and infections
  Causes long-term disability and may lead to death
Diagnosed by medical and occupational health history as well as Pulmonary Function Tests (PFT) (preferred, if available)
Notes: https://www.cdc.gov/copd/infographics/copd-awareness.html

## Slide 38: Smoking & Silica
Cigarette smoking exacerbates lung damage caused by silica, and contributes significantly to the development of lung disease.

## Slide 39: Diseases of Silica: Non-Lung Diseases
Some evidence that exposure increases risk of kidney disease
Some evidence that exposure increases risk of scleroderma
  Patients may have thickened skin, stiff joints, tiredness, and poor blood flow
Notes: Not sure if this is public domain…

## Slide 40: Review of health effects
This video is a good review of how breathing in silica dust can cause permanent damage to the lungs.
https://www.youtube.com/watch?v=R_sC2wX9Uwc

## Slide 41
Could this exposure cause health effects ?

## Slide 42: How do you know which employees are being exposed?

## Slide 43: Risk Assessment
Hazard-anything that may cause harm
Risk-severity and likelihood that exposure to a hazard will cause injury or disease
Risk assessment includes
  Determining how likely something is to cause harm?
  What actions can protect you?

## Slide 44: Workplace Exposure Limits
Workplace Exposure Standards (WESs) help to assess and communicate risk
A WES is an acceptable upper limit of exposure
Sampling requires testing with pumps and analyzing samples at a laboratory
  Expensive and few laboratories offer the proper analysis
  Must use size-selected results to compare to an WES
Rule of thumb: If you see dust, there is likely respirable dust and you have a problem!!!

## Slide 45: Measurement of the concentration of silica
Can be used to assess the performance of controls
It will identify where the exposures are the highest
Enable the improvement of the controls using the hierarchy :
  Elimination
  Substitution
  Engineering
  Administrative
  PPE – Respiratory protection
Resulting in the improvement of the health and productivity of the workforce

## Slide 46: Measuring exposure to silica
Dust particles from the air are pulled into a sampling device using a pump and collected onto a filter
The smaller sized respirable particles must be separated from the larger particles when measuring exposures using a size-selective device
  Traditional Cyclone
Need to take multiple samples due to variability

## Slide 47: Air sampling for silica
The flow rate of the sampling pump must be carefully calibrated to
  make sure that it is collecting the correct size
  calculate the total volume of air sampled
The filters will be sent to a laboratory and analyzed for crystalline content using either methods
  Infrared analysis (IR)
  X-Ray diffraction (XRF)
The filter is also weighed before and after sampling to determine the total weight of respirable dust
Only in the U.S., you must find the percentage of crystalline silica by calculating the weight of the crystalline silica content divided by the total weight of the dusts

## Slide 48: Proper sampling for silica
The sampling pump should be worn for the entire duration of the work shift
  Those results can be compared to workplace exposure standard
Please check your national regulations concerning respirable silica exposure standards.
The Safe Work Australia, workplace exposure standard (WES) is 0.05mg/m3, 8 hour time weighted average.

## Slide 49: Sampling Procedures for Silica
There are some videos to show the different types of sampling available
  Calibration with an aluminum cyclone: https://www.youtube.com/watch?v=LqiY2acDIgM
  Assembly and Collection of silica with cyclones: https://www.youtube.com/watch?v=O5knJEGGa7k
  NIOSH Sampling with Aluminum Cyclone: https://www.youtube.com/watch?v=9LPzWn9GchQ
  Parallel Particle Impactor (PPI): https://www.youtube.com/watch?v=Mrc7uQC7VAY

## Slide 50: Recommendations
“There can be no intelligent control of the…danger in industry unless it is based on the principle of keeping the air clear from dust and fumes.” – Alice Hamilton
Occupational hygiene and air sampling is the backbone of occupational health, driving recommendations
WES are often the basis for assessing risk, making recommendations, and instituting controls
Notes: Quote from this: https://www.brainyquote.com/authors/alice_hamilton

## Slide 51: How do I prevent people from being exposed?

## Slide 52: Hierarchy of Controls
Elimination
Substitution
Engineering controls
  WWwet methods
  Isolate the process
  Isolate the worker
Administrative Controls
Personal protective equipment
Notes: Image from https://www.cdc.gov/niosh/topics/hierarchy/default.html

## Slide 53: Elimination or Substitution
Elimination - Abrasive blasting with sand (sandblasting) has been banned in Australia starting in 1959 in NSW
Substitution - with other material for the sand, such as:
  Metal beads, steel shot
  Chemicals can be used to remove surface coatings
    Be aware of the hazards of the chemical
  High pressure water
    Used in bridge deck refurbishing
Notes: https://www.cdc.gov/niosh/docs/92-102/default.html

## Slide 54: Substitution: Tragedy of the Jeans
Manufacturers of jeans in Turkey
Used sandblasting for a “weathered” look
Sand was used to blast jeans without controls
  Over 50 workers died
  Many more suffered irreversible lung disease
  Could have all been avoided by substitution!
Notes: Don’t know if this picture is copyrighted….

## Slide 55: Engineering Controls
Change the process to reduce exposure
  Retrofitting or purchasing equipment capable of wet methods for cutting, sawing, etc.
Enclosing the process to remove the worker from the hazard
  Glove box
  Covers on conveyor belts
  Ventilation
  Cabs for construction/mining equipment
Visual dust emissions indicate that a control is needed
Engineering controls (primarily wet methods) found to be the most cost-effective silica control strategy in developing and developed countries

## Slide 56: Engineering controls resources
Some of the most effective and feasible engineering controls are
  Wet Methods (requires Water most effective)
  Dry Methods (requires ELECTRICITY)
Here is a link to several videos showing engineering controls
https://www.silica-safe.org/whats-working/controlling-silica-dust-learning-from-each-other

## Slide 57: Engineering Controls: Wet Methods
Wet methods can significantly reduce exposures, but require pre-planning
  Cutting with saws equipped with water basin
  Drilling with water pump through the drill stem
  Grinding and hammering on pre-wetted surfaces
  Fogging or steaming to suppress dust in areas where dust is generated
    water spray misting is important to reduce exposure to smaller particles

## Slide 58: Engineering Controls: Wet methods
Dry sawing concrete
Wet sawing concrete water is added at
saw blade
Notice puddle at feet of wet saw operator. It contains the same amount of dust as seen in picture of dry saw operator. What happens to the dust when puddle dries?
Pictures from OSHA

## Slide 59: Engineering Controls: Wet methods
Here is a video to show some wet methods that might be available in a construction setting: https://www.youtube.com/watch?v=f5Ec4TrzN4Y

## Slide 60: Engineering Controls: Dry Methods
The most common dry collection method is vacuum dust collection and the specific filter required is H class, but may be more expensive and require electricity.
  Cutting with a vacuum system affixed to the saw blade
  Drilling with an enclose around where the drill enters the surface
  Grinding with a shroud that surrounds the grinding wheel
https://www.youtube.com/watch?v=_Ia1zp777Ik

## Slide 61: Example of Tool Selection during Concrete Drilling
Wet Methods
Pneumatic (powered by compressed air)
High exposures
Dry Methods
Pneumatic (powered by compressed air)
Higher exposures
Wet Methods
Electric
Lowest exposures
Dry Methods
Electric
Higher exposures

## Slide 62: Engineering Controls: Isolate the Process
Using a glove box for sandblasting
Using covers on conveyor belts and/or lowering the drop heights from conveyor belts
Enclosure for dumping
  Ventilation
  Wetting (1% moisture by weight)
    Activate with photocell or mechanical switch
Notes: Conveyor picture: https://www.cdc.gov/niosh/docs/2015-105/pdfs/2015-105.pdf

## Slide 63: Administrative Controls
Recommend procedures to:
  Perform routine housekeeping to reduce the build up of dust in the work area
  Prohibit dry sweeping and implement wet sweeping methods
  If services are available, institute a medical monitoring program
  In vehicles and mobile equipment, implement windows closed, door seals checked in pre-start and air con operating correctly.
Educate and train employees on the hazards of working with RCS

## Slide 64: Education & Training
It is important for employees to:
  Be informed of the hazards of working with silica
  Be able to recognize when the hazard is present
  Know how to prevent themselves from being exposed
  Know how to operate engineering controls
  Be familiar with required PPE and how to wear it
The Center for Construction Research and Training has good guidance on silica trainings
  https://www.silica-safe.org/training-and-other-resources

## Slide 65: Personal Protective Equipment (PPE)
Respirators may be of immediate assistance
  Half-face
  Full-face
  Filtering face piece
Respirators are a good method to prevent exposure if engineering controls aren’t in place, but they have limitations, including:
  Highly dependent on seal
  Require regular change-out
Respirators must be fit- tested by an accredited fit- tester to ensure they seal onto the face.
Go to RESP-FIT website, https://respfit.org.au/
Notes: https://www.cdc.gov/niosh/npptl/

## Slide 66: Fit Testing of Respirators
RESP-FIT was established to improve worker health protection of those wearing tight fitting respiratory protective equipment, through reliable respirator fit testing by competent fit testers in Australia.

## Slide 67: What can employees do?
Use all available engineering controls such as blasting cabinets and local exhaust ventilation.
Do not use compressed air for cleaning surfaces.
Use water sprays, wet methods (e.g. wet spray misting) for cutting, chipping, drilling, sawing, grinding, etc.
Substitute non-crystalline silica blasting material.
Use respirators approved for protection against silica; if sandblasting, use abrasive blasting respirators.
Do not eat, drink or smoke near crystalline silica dust.
Wash hands and face before eating, drinking or smoking away from exposure area.
Quit smoking
Notes: https://www.osha.gov/Publications/silicosis.html

## Slide 68: Control Banding
Control banding is a method that uses
  severity of the chemical
  quantity of the chemical
  likelihood of exposure to the chemical
Based on those, control banding recommends a level of exposure control
  General ventilation
  Engineering controls
  Containment
  Special

## Slide 69: Control Banding for Silica
Control banding for silica is typically based on the industry, and recommends controls based on the common tasks in the industry
COSHH Essentials. To help employers reduce exposures COSHH created a series of informative guides
  COSHH Silica Essentials Direct Advice http://www.hse.gov.uk/pubns/guidance/
  Translated into Spanish by ILO
  http://www.ilo.org/legacy/spanish/protection/safework/coshh_essentials_silica/index.htm
  NEPSI (Noyau Europeen pour la Silice) Good Practice Guide
  https://www.nepsi.eu/good-practice-guide

## Slide 70: Take Home Messages
Crystalline silica is a mineral found everywhere and airborne particles are dangerous
Cutting, grinding and other activities break down the mineral into small parts and leads to airborne dust exposure
Inhaling very small crystalline silica particles causes multiple diseases, including silicosis, an incurable lung disease that can lead to disability and death
Use occupational hygiene air monitoring methods to collect the fine respirable sized dust and compare the respirable crystalline silica exposure to the WES

## Slide 71: Take Home Messages
Remember, if you working with substances containing crystalline silica - if you can see the dust then you know there is a problem AND if you cannot see the fine dust you may still have a problem
Apply the hierarchy of controls to minimise exposures
Keep it wet!!!

## Slide 72: QUESTIONS/COMMENTS